## Slide 1: TS2 Conveyor Control – TwinCAT Solution
Modular PLC program for Bosch TS2 conveyor with LTUs & stoppers
Developed in TwinCAT 3
Supports direct, corner, orange, and multi-hop transfers
Includes scheduler, simulation, and homing

## Slide 2: System Overview
Devices
  4 Blue stoppers (entry points, each with a reader)
  4 Purple stoppers (at LTU interfaces)
  4 LTUs (Lift-Transfer Units: NE, SE, SW, NW corners)
  Continuous conveyors (Green/Orange lines)
Carriers
  Detected by Readers at stoppers
  Routed based on destination tag

## Slide 3: Core Logic
Function Blocks (FBs)
  FB_Stopper → controls block/release, simulates Occupied
  FB_LTU → handles lift, push, sensors (LB, Occupied)
  FB_Reader → generates Valid pulse + Destination value
  FB_DirectTransfer, FB_TransferCorner, FB_TransferChain
State Machines
  Each transfer path (e.g. 12→6, 3→9, 12→9) has its own state machine
  Steps: IDLE → Release → LTU cycles → Complete/Error

## Slide 4: Scheduler + Homing
Scheduler
  Single-shot or Queue version (FIFO)
  Dispatches transfer requests when Busy=FALSE
  Handles multiple carriers arriving close together
Homing
  FB_HomingLTU → moves LTU to Bottom (reference)
  FB_HomingManager → runs homing for all LTUs
  Scheduler enabled only after homing completes

## Slide 5: Benefits
Modular, reusable FBs
Supports testing without hardware
Extendable to real I/O with minimal changes
Clear separation: Initialization → Scheduling → Transfer execution